### 104.1 Create partitions and filesystems

Configure disk partitions and create filesystems or swap space on media such as hard disks, and design a disk partitioning scheme for a Linux system. Tasks include understanding the different types of common Linux filesystems, and allocating filesystems and swap space to separate partitions or disks.

Block device is an abstraction layer for storage devices
ls -l dev → b for block (hdd, ssd, cdrom etc …), c for character (terminal etc …)

The partition table of a disk will contain info about the beginning and the end of the different partitions, the type of partition and also if its a bootable one or not. It will be possible, as a root, to check this partition table with the fdisk tool.
The star character means that the partition is bootable.
Ext2 = used in early versions of linux
ext3 = ext 2 + journaling
ext4 = ext3 for larger filesystems
ReiserFS = good for a lot of small files
vfat = fat32
Other tools like parted/gparted to have more attractive interface for partitions management
fdisk ( for 'fixed disk' or cfisk which is more beautiful)
fdisk -l /dev/sda = list partitions from sda
allow user to edit partition table : create or remove partitions
dont forget to backup data and boot from live cd or usb to ensure that partitions are no in use already
edit partition table : fdisk /dev/sda (opens menu)
m = help
a = sets a bootable flag
p = displays existing partitions for disk
n= new partition => select logical(l) or primary (p) => select number => set first cylinder or size
t = change partition type => select partition number => code (listed with L option)
q = quit without saving
v = verify and w = write

mkfs
create filesystem
ext2 = mkfs.ext2 = -type ext2 = mk2fs
ext3 = mkfs.ext3
ext4 = mkfs.ext4
ReiserFS = mkfs.reiserfs
list of installed ones = ls /sbin/mk*
create ext3 fs = mkfs -t ext3 /dev/sda8µ
UUID = universal unique identifier
display UUID of disk : blkid /dev/sda8
use GPT instead of MBR layout (display only) : gdisk -l /dev/sdc
create GPT and a partition : gdisk /dev/sdc
create ext4 partition : mkfs -t ext4 -L IAN-USB32 /dev/sdc1
create xfs fs : mkfs -t xfs -i size=512 /dev/sda8
create vfat(fat32) fs : mkfs -t vfat /dev/sda9

mke2fs
creates a Linux ext2, ext3 and ext4 FS

mkswap
create swap space
mkswap /dev/sda4
enable swap space : swapon <> swapoff to disable
and create an entry in fstab to keep it permanently (genfstab or manually ?)
Objectives
Use various mkfs commands to set up partitions and create various filesystems such as:
ext2/ext3/ext4
xfs
reiserfs v3
vfat

Todo
Learn more about GPT (GUID Partition Table) and MBR (Master Boot Record) layers
Train to create mkfs
Sources
Partitions : http://www.tldp.org/LDP/sag/html/partitions.html
Speedup SSD by aligning partitions : http://lifehacker.com/5837769/make-sure-your-partitions-are-correctly-aligned-for-optimal-solid-state-drive-performance
Disk alignment : http://homepage.ntlworld.com./jonathan.deboynepollard/FGA/disc-partition-alignment.html
4kb sector disks : http://www.ibm.com/developerworks/linux/library/l-4kb-sector-disks/
Questions
1. Typing fdisk -l /dev/sda on a Linux computer with an MBR disk produces a listing
of four partitions: /dev/sda1, /dev/sda2, /dev/sda5, and /dev/sda6. Which of the
following is true?
A. The disk contains two primary partitions and two extended partitions.
B. Either /dev/sda1 or /dev/sda2 is an extended partition.
C. The partition table is corrupted; there should be a /dev/sda3 and a /dev/sda4 before
     /dev/sda5.
D. If you add a /dev/sda3 with fdisk, /dev/sda5 will become /dev/sda6 and /dev/
  sda6 will become /dev/sda7.
E.Both /dev/sda1 and /dev/sda2 are logical partitions.

2.A new Linux administrator plans to create a system with separate /home, /usr/local, and
/etc partitions, in addition to the root (/) partition. Which of the following best describes
this configuration?
A. The system won’t boot because critical boot-time files reside in /home.
B. The system will boot, but /usr/local won’t be available because mounted partitions
 must be mounted directly off their parent partition, not in a subdirectory.
C. The system will boot only if the /home partition is on a separate physical disk from the
     /usr/local partition.
D. The system will boot and operate correctly, provided each partition is large enough for
  its intended use.
E. The system won’t boot because /etc contains configuration files necessary to mount
 non-root partitions.
3. Which of the following directories is most likely to be placed on its own hard disk parti-
tion?
A. /bin
B. /sbin
C. /mnt
D. /home
E. /dev
4. You run Linux’s fdisk and modify your partition layout. Before exiting the program,
you realize that you’ve been working on the wrong disk. What can you do to correct this
problem?
A. Nothing; the damage is done, so you’ll have to recover data from a backup.
B. Type w to exit fdisk without saving changes to disk.
C. Type q to exit fdisk without saving changes to disk.
D. Type u repeatedly to undo the operations you’ve made in error.
E. Type t to undo all the changes and return to the original disk state.

5. What does the following command accomplish?
# mkfs -t ext2 /dev/sda4
A. It sets the partition table type code for /dev/sda4 to ext2.
B. It converts a FAT partition into an ext2fs partition without damaging the partition’s
    existing files.
C. Nothing; the -t option isn’t valid, and so it causes mkfs to abort its operation.
D. It converts an ext2 filesystem to an ext4 filesystem.
E. It creates a new ext2 filesystem on /dev/sda4, overwriting any existing filesystem and
  data.

6. Which of the following best summarizes the differences between DOS’s FDISK and Linux’s
fdisk?
A. Linux’s fdisk is a simple clone of DOS’s FDISK but written to work from Linux rather
than from DOS or Windows.
B. The two are completely independent programs that accomplish similar goals, although
  Linux’s fdisk is more flexible.
C. DOS’s FDISK uses GUI controls, whereas Linux’s fdisk uses a command-line interface,
      but they have similar functionality.
D. Despite their similar names, they’re completely different tools—DOS’s FDISK handles
        disk partitioning, whereas Linux’s fdisk formats floppy disks.
E. DOS’s FDISK manages GPT disks whereas Linux’s fdisk manages MBR disks.