### 104.3 Control mounting and unmounting of filesystems

Configure the mounting of a filesystem. Tasks include manually mounting and unmounting filesystems, configuring filesystem mounting on bootup, and configuring user-mountable removable filesystems.
Linux tree is rooted by /. Mount = process of making the FS accessible on the device, mapping a disk partition to a directory
mount command = mount temporarily <> edit /etc/fstab = mount at each boot
/etc/fstab (filesystem table)
contains static info about filesystems
/media
mount point for removables medias : cdroms, floppy etc ...
/mnt similar but made for admin to mount points manually
a usb device plugged would result in a new dir in /media, not mnt

/etc/mtab
list of currently mounted FS (can use df as well)

mount
mount the filesystem on the device = mount the device
mount command = /proc/mounts
mount /dev/sda9 /dos
the mount point /dos must exist before
mount -t vfat /dev/xxx /xxx = specify mounting type
mount – displays mounted fs
mount -a : mounts all FS in /etc/fstab
-r : mount readonly
-v : verbose mode
-w : mounts read/write
-o rw : same as -w
-t xxx : specifieds FS type
can display infos with cat /proc/mounts and cat /etc/mtab
mount read only (remount if already exists) : mount -o remount,ro /dos
it is also possible to mount with the UUID or label of the device
umount
unmount a fs by specifying either the device name or mount point
umount /dev/sdax or umount /proc
umount -a : unmounts all FS in /etc/mtab
-f : forces to unmount a FS
-r : if can't unmount a FS, then rolls it back to a read only
-t xxx : specifies a FS type (same as mount)

lsof
lists open files
lsof -w /proc
fuser
identify processes using files or sockets
fuser -m /proc
id
prints users and group information
Objectives
Manually mount and unmount filesystems.
Configure filesystem mounting on bootup.
Configure user mountable removeable filesystems.
Todo
Sources
media/ : http://www.tldp.org/LDP/Linux-Filesystem-Hierarchy/html/media.html

Questions

1. To access files on a USB flash drive, you type mount /dev/sdc1 /media/flash as root.
Which types of filesystems will this command mount?
A. Ext2fs
B. FAT
C. HFS
D. ReiserFS
E. All of the above
2. Which of the following /etc/fstab entries will mount /dev/sdb2 as the /home directory
at boot time?
A. /dev/sdb2 reiserfs /home defaults 0 0
B. /dev/sdb2 /home reiserfs defaults 0 0
C. /home reiserfs /dev/sdb2 noauto 0 0
D. /home /dev/sdb2 reiserfs noauto 0 0
E. reiserfs /dev/sdb2 /home noauto 0 0
3. What filesystem options might you specify in /etc/fstab to make a removable disk
(USB flash drive, Zip disk, floppy disk, and so on) mountable by an ordinary user with a
UID of 1000? (Select three.)
A. user
B. users
C. owner
D. owners
E. uid=1000

4. What is the minimum safe procedure for removing a USB flash drive, mounted from /dev/
sdb1 at /media/usb, from a Linux computer?
A. Type umount /media/usb, wait for the command to return and disk-activity lights to
stop, and then unplug the drive.
B. Unplug the drive, and then type umount /media/usb to ensure that Linux registers the
  drive’s removal from the system.
C. Unplug the drive, and then type sync /dev/sdb1 to flush the caches to ensure prob-
  lems don’t develop.
D. Type usbdrive-remove, and then quickly remove the disk before its activity light stops
  blinking.
E. Type fsck /dev/sdb1, wait for the command to return and disk-activity lights to stop,
  and then unplug the drive.